Key Features

- 50 Ohm Impedance

- 1.0 ~ 2.0 GHz

- 0.7 dB Noise Figure

- 28 dB Gain

- 1.25:1 VSWR

- Built-in input & output limiter

- Precision Machined Housing

- Single DC Power Supply

Applications

- GPS,DCS

- RF Bench Tests

- Receiver Amplifiers

- Mobile Base Station Applications

Absolute Maximum Ratings

| Parameters | Units | Ratings |
| --- | --- | --- |
| DC Power Supply Voltage | V | -0.5,+32 |
| RF Input CW Power | dBm | 30 |
| Storage Temperature | °C | -40 ~ +85 |
| Operating Temperature | °C | -40 ~ +85 |

Operation of this device beyond any one of these parameters may cause permanent damage.

Specifications

Summary of the key electrical specifications at 25°C

| Index | Testing Item | Symbol | Test Constraints | Min | Nom | Max | Unit |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Frequency Range | BW | 50 Ohm Impedance | 1200 |  | 1600 | MHz |
| 2 | Gain | S21 | 1145 – 1616 MHz | 26.5 | 28 | 29.5 | dB |
| 3 | Gain Variation | (G | 1145 – 1616 MHz |  | +/- 0.7 |  | dB |
| 4 | VSWR | SWRi | 1145 – 1616 MHz, all RF ports |  | 1.25:1 | 1.65:1 | Ratio |
| 5 | Reverse Isolation | S12 | 1145 – 1616 MHz |  | 42 |  | dB |
| 6 | Noise Figure | NF | 1145 – 1616 MHz |  | 0.7 | 1.0 | dB |
| 7 | Output Power 1dB Compression Point | P1dB | 1145 – 1616 MHz |  | 1 |  | dBm |
| 8 | Current Consumption | Idd | Vdd = +12.0 V |  | 21 |  | mA |
| 9 | Power Supply Operating Voltage | Vdd |  | +7 | +12 | +16 | V |
| 10 | Operating Temperature | To |  | -40 |  | +85 | oC |
| 11 | Thermal Resistance | Rth,c | Junction to case |  |  | 215 | oC/W |

Functional Block Diagram                              Outline, IP-3 Housing

Typical Data

Application Notes:

- SMA Torque Wrench Selection

Always use a torque wrench with 5 ~ 6 inch-lb coupling torque setting for mating the SMA cables to the amplifier. Never use torque more than 8 inch-lb wrench for tightening the mating cable to the connector. Otherwise, the permanent damage will occur to the SMA connectors of the amplifier. 8710-1582 (5 inch-lb) is one of the ideal torque wrench choice from Agilent Technology.

- Mounting the Amplifier

Use three pieces of #2-56 with longer than 9/16” screws for mounting the amplifier on a metal-based chase. Flat and spring washers are needed to prevent the screw loosening during the shock and vibration. Always use the appropriate torque setting of the power screwdriver to mount them.

******

# Text boxes

Ordering Information

| Model Number | Connectors |
| --- | --- |
|  | IN | OUT |
| ILA120160L | SMA Female | SMA Female |